Company logo	AFMS	Doc No:
		Revision:
		Date:
Company approval reference, if any	Standard Change / Standard Repair reference	Page:

TITLE

A/C :
Version :
S/N :
Registration :
This Aircraft Flight Manual Supplement (AFMS) must be attached to the approved AIRCRAFT FLIGHT MANUAL (AFM) kept on board the aircraft.
The information contained in this document integrates and, in some cases, supersedes the information reported in the corresponding section of the approved AFM.

LIST OF EFFECTIVE PAGES

Page	Edition — Revision — Date	Page	Edition — Revision — Date

LIST OF EDITION/REVISION INCORPORATED
Edition	Revision	Data	Description	Page

GENERAL
Introduction
An AFM supplement (AFMS) should normally cover only a single system, device or piece of equipment, such as an autopilot, ski, or navigation system.
The AFMS should follow the same structure as the basic AFM to which the supplement applies (the same numbering of points/paragraphs, same layout). It should use the same terminology and definitions and, whenever applicable, present normal and emergency procedures in the same way they are presented in the basic AFM.
Each supplement should be a self-contained, miniature flight manual with at least the following:
Scope
The purpose of the supplement and the system or equipment to which it specifically applies should be stated.
Limitations
Any change to the limitations, markings or placards of the basic AFM should be stated. If there is no change, a statement to that effect should be made. Refer also to point CS STAN.20 in Subpart A.
Emergency procedures
Any addition or change to the basic emergency procedures of the AFM should be stated. If there is no change, a statement to that effect should be made.
Normal procedures
Any addition or change to the basic normal procedures of the AFM should be stated. If there is no change, a statement to that effect should be made.
Performance
Any effect of the given installation upon the performance of the aircraft as shown in the basic AFM should be indicated. If there is no change, a statement to that effect should be made.
Weight and balance
Any effect of the given installation upon the weight and balance of the aircraft should be indicated. If there is no change, a statement to that effect should be made.

---- end ----